## Slide 1
Chapter 2:
Combinational Logic Design
Digital Design &
Computer Architecture
Sarah Harris & David Harris

## Slide 2
Chapter 2 :: Topics
Combinational Circuits
Boolean Equations
Boolean Algebra
From Logic to Gates
X’s and Z’s, Oh My
Karnaugh Maps
Combinational Building Blocks
Timing

## Slide 3
Chapter 2: Combinational Logic
Combinational Circuits

## Slide 4
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 5
Nodes
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
Circuit elements
  E1, E2, E3
  Each a circuit
Circuits

## Slide 6
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs
Types of Logic Circuits

## Slide 7
Every element is combinational
Every node is either an input or connects to exactly one output
The circuit contains no cyclic paths
Example:
Rules of Combinational Composition

## Slide 8
Chapter 2: Combinational Logic
Boolean Equations

## Slide 9
Functional specification of outputs in terms of inputs
Example: S = F(A, B, Cin)
Cout = F(A, B, Cin)
Boolean Equations

## Slide 10
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Minterm: product that includes all input variables
ABC, ABC, ABC
Maxterm: sum that includes all input variables
(A+B+C), (A+B+C), (A+B+C)
Some Definitions

## Slide 11: Sum-of-Products Form
Y = F(A, B) =
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form
0
1
0
1

## Slide 12: Sum-of-Products Form
Y = F(A, B) = AB + AB = Σ(1, 3)
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form
Short-hand
Long-hand

## Slide 13
Y = F(A, B) = (A + B)●(A + B) = Π(0, 2)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form
Short-hand
Long-hand

## Slide 14
Boolean Equations Example
You are going to the cafeteria for lunch
  You won’t eat lunch (E = 0)
    If it’s not clean (C = 0) or
    If they only serve meatloaf (M = 1)
Write a truth table for determining if you will eat lunch (E).

## Slide 15
SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 16
E = (C + M)(C + M)(C + M)
= Π(0, 1, 3)
E = CM
= Σ(2)
SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 17
Forming Boolean Expressions
Example 1:
We will go to the Park (P is the output) if it’s not Raining (R) and we have Sandwiches (S).
Boolean Equation:
P = RS

## Slide 18
Forming Boolean Expressions
Example 2:
You will be considered a Winner (W is the output) if we send you a Million dollars (M) or a small Notepad (N).
Boolean Equation:
W = M + N

## Slide 19
Forming Boolean Expressions
Example 3:
You can Eat delicious food (E is the output) if you Make it yourself (M) or you have a personal Chef (C) and she/he is talented (T) but not eXpensive (X).
Boolean Equation:
E = M + CTX

## Slide 20
Forming Boolean Expressions
Example 4:
You can Enter the building if you have a Hat and Shoes on or if you have a Hat on.
Boolean Equation:
E = HS + H

## Slide 21
Forming Boolean Expressions
Example 5:
You can Enter the building if you have a Hat and Shoes on or if you have a Hat and no Shoes on.
Boolean Equation:
E = HS + HS

## Slide 22
Chapter 2: Combinational Logic
Boolean Algebra: Axioms

## Slide 23
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged
Boolean Algebra

## Slide 24
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 25
Boolean Axioms
Number | Axiom | Dual | Name
A1 | B = 0 if B ≠ 1 | B = 1 if B ≠ 0 | Binary Field
A2 | 0 = 1 | 1 = 0 | NOT
A3 | 0 • 0 = 0 | 1 + 1 = 1 | AND/OR
A4 | 1 • 1 = 1 | 0 + 0 = 0 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | 1 + 0 = 0 + 1 = 1 | AND/OR
Dual: Replace: • with +
0 with 1

## Slide 26
Chapter 2: Combinational Logic
Boolean Algebra: Theorems of
One Variable

## Slide 27
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements
Dual: Replace: • with +
0 with 1

## Slide 28
Boolean Theorems of One Variable
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 29
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 30
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 31
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 32
B = B
T4: Identity Theorem

## Slide 33
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 34
Recap: Basic Boolean Theorems
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements

## Slide 35
Chapter 2: Combinational Logic
Boolean Algebra: Theorems of
Several Variables

## Slide 36
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Boolean Theorems of Several Vars
Warning: T8’ differs from traditional algebra:
OR (+) distributes over AND (•)

## Slide 37
How to Prove
Method 1: Perfect induction
Method 2: Use other theorems and axioms to simplify the equation
  Make one side of the equation look like the other

## Slide 38
Proof by Perfect Induction
Also called: proof by exhaustion
Check every possible input value
If the two expressions produce the same value for every possible input combination, the expressions are equal

## Slide 39
T9: Covering
Prove true by:
Method 1: Perfect induction
Method 2: Using other theorems and axioms
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 40
T9: Covering
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 41
T9: Covering
Method 2: Prove true using other axioms and theorems.
B•(B+C) = B•B + B•C T8: Distributivity
= B + B•C T3: Idempotency
= B•1 + B•C T2: Null Element
= B•(1 + C) T8: Distributivity
= B•(1) T2: Null element
= B T1: Identity
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 42
T10: Combining
Prove true using other axioms and theorems:
B•C + B•C = B•(C+C) T8: Distributivity
= B•(1) T5’: Complements
  = B T1: Identity
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | Combining

## Slide 43
De Morgan’s Theorem: Dual
The complement of the product is the
sum of the complements.
Dual:
The complement of the sum is the
product of the complements.
# | Theorem | Dual | Name
T12 | B•C•D… = B+C+D… | B+C+D…= B•C•D… | De Morgan’s Theorem

## Slide 44
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
T12 | B•C•D… = B+C+D… | B+C+D…= B•C•D… | De Morgan’s
Recap: Theorems of Several Vars

## Slide 45
Chapter 2: Combinational Logic
Boolean Algebra: Simplifying Equations

## Slide 46
Simplifying an Equation
Simplifying may mean minimal sum of products form:
SOP form that has the fewest number of implicants, where each implicant has the fewest literals
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C
Simplifying could also mean fewest number of gates, lowest cost, lowest power, etc. For example, Y = A xor B is likely simpler than minimal Sum of Products Y = AB + AB. These depend on details of the technology.

## Slide 47
Y = AB + AB
Y = B T10: Combining
or
Y = B(A + A) T8: Distributivity
= B(1) T5’: Complements
= B T1: Identity
Simplifying Boolean Equations
Example 1:
Recommended Method

## Slide 48
Y = ABC + ABC + ABC
= ABC + ABC + ABC + ABC T3’: Idempotency
= (ABC+ABC) + (ABC+ABC) T7’: Associativity
= AC + BC T10: Combining
Simplifying Boolean Equations
Example 2:

## Slide 49
Chapter 2: Combinational Logic
Boolean Algebra: Simplifying Equations
Extra Examples

## Slide 50
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Idempotency (duplication) A = A + A
“Simplification” theorem A + AP = A + P
    A + AP = A + P

## Slide 51
Proving the “Simplification” Theorem
“Simplification” theorem
A + AP = A + P
Method 1: A + AP = A + AP + AP T9’ Covering
= A + (AP + AP) T7 Associativity
= A + P T10 Combining
Method 2: A + AP = (A + A) (A + P) T8’ Distributivity
= 1• (A + P) T5’ Complements
= A + P T1 Identity

## Slide 52
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove using other theorems and axioms:
B•C + B•D + C•D
= BC + BD + (CDB+CDB) T10: Combining
= BC + BD + BCD+BCD T6: Commutativity
= BC + BCD + BD + BCD T6: Commutativity
= (BC + BCD) + (BD + BCD) T7: Associativity
= BC + BD T9’: Covering

## Slide 53
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Idempotency (duplication) A = A + A
“Simplification” theorem A + AP = A + P
    A + AP = A + P

## Slide 54
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Idempotency (duplication) A = A + A
“Simplification” theorem A + AP = A + P
    A + AP = A + P

## Slide 55
Y = A(AB + ABC)
= A(AB(1 + C)) T8: Distributivity
= A(AB(1)) T2’: Null Element
= A(AB) T1: Identity
= (AA)B T7: Associativity
= AB T3: Idempotency
Simplifying Boolean Equations
Example 3:

## Slide 56
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Idempotency (duplication) A = A + A
“Simplification” theorem A + AP = A + P
    A + AP = A + P

## Slide 57
Y = A’BC + A’ Recall: A’ = A
Note:
A‘ is shorthand for A.
But use the tick symbol (‘) only when typing.
It’s easy to lose ticks (‘) when writing by hand!
It is strongly recommended that you simplify equations by writing by hand.
Simplifying Boolean Equations
Example 4:

## Slide 58
Y = A’BC + A’ Recall: A’ = A
= A’ T9’ Covering: X + XY = X
or
= A’(BC + 1) T8: Distributivity
= A’(1) T2’: Null Element
= A’ T1: Identity
Simplifying Boolean Equations
Example 4:

## Slide 59
An expression is in sum-of-products (SOP) form when all products contain literals only.
SOP form: Y = AB + BC’ + DE
NOT SOP form: Y = DF + E(A’+B)
SOP form: Z = A + BC + DE’F
Multiplying Out: SOP Form

## Slide 60
Multiplying Out: SOP Form
Example 5:
This method is called multiplying out.
Y = (A + C + D + E)(A + B)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = (C+D+E), Z = B and rewrite equation
Y = (A+X)(A+Z) substitution (X=(C+D+E), Z=B)
= A + XZ T8’: Distributivity
= A + (C+D+E)B substitution
= A + BC + BD + BE T8: Distributivity
or
Y = AA+AB+AC+BC+AD+BD+AE+BE T8: Distributivity
= A+AB+AC+AD+AE+BC+BD+BE T3: Idempotency
= A + BC+BD+BE T9’: Covering
Recommended Method

## Slide 61
Y = AB + BC +B’D’ + AC’D’
Method 1:
Y = AB + BC + B’D’ + (ABC’D’ + AB’C’D’) T10: Combining
= (AB + ABC’D’) + BC + (B’D’ + AB’C’D’) T6: Commutat.
T7: Associativity
= AB + BC + B’D’ T9: Covering
Method 2:
Y = AB + BC + B’D’ + AC’D’ + AD’ T11: Consensus
= AB + BC + B’D’ + AD’ T9: Covering
= AB + BC + B’D’ T11: Consensus
Simplifying Boolean Equations
Example 6:

## Slide 62
Literal and implicant ordering
Variables within an implicant should be in alphabetical order.
The order of implicants doesn’t matter.
  Examples:
  Correct: Y = AB + BC + BD
  Correct: Y = BC + BD + AB
  Incorrect: Y = CB + BD + BA
  Incorrect: Y = AB + BC + DB

## Slide 63
Simplifying Boolean Equations
Example 7:
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + BCDE T9’: Covering
= A + BCDE T9’: Covering
Recommended Method

## Slide 64
E = (C + M)(C + M)(C + M)
= (C + MM)* (C + M)
= (C + 0)* (C + M)
= C * (C + M)
= CC + CM
= 0 + CM
= CM
E = CM
Review: Canonical SOP & POS Forms
SOP – sum-of-products
POS – product-of-sums
same

## Slide 65
An expression is in product-of-sums (POS) form when all sums contain literals only.
POS form: Y = (A+B)(C+D)(E’+F)
NOT POS form: Y = (D+E)(F’+GH)
POS form: Z = A(B+C)(D+E’)
Factoring: POS Form

## Slide 66
Factoring: POS Form
Example 8:
Y = (A + B’CDE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = B’C, Z = DE and rewrite equation
Y = (A+XZ) substitution (X=B’C, Z=DE)
= (A+B’C)(A+DE) T8’: Distributivity
= (A+B’)(A+C)(A+D)(A+E) T8’: Distributivity

## Slide 67
Factoring: POS Form
Example 9:
Y = AB + C’DE + F
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: W = AB, X = C’, Z = DE and rewrite equation
Y = (W+XZ) + F substitution W = AB, X = C’, Z = DE
= (W+X)(W+Z) + F T8’: Distributivity
= (AB+C’)(AB+DE)+F substitution
= (A+C’)(B+C’)(AB+D)(AB+E)+F T8’: Distributivity
= (A+C’)(B+C’)(A+D)(B+D)(A+E)(B+E)+F T8’: Distributivity
= (A+C’+F)(B+C’+F)(A+D+F)(B+D+F)(A+E+F)(B+E+F) T8’: Distr.

## Slide 68
Y = (A+BD)C
= (A+BD) + C
= (A•(BD)) + C
= (A•(BD)) + C
= ABD + C
De Morgan’s Theorem
Work from the outside in
(i.e., top bar, then down)
Use involution when possible
Example 10:

## Slide 69
Y = (ACE+D) + B
= (ACE+D) • B
= (ACE•D) • B
= ((AC+E)•D) • B
= ((AC+E)•D) • B
= (ACD + DE) • B
= ABCD + BDE
De Morgan’s Theorem
Example 11:

## Slide 70
Chapter 2: Combinational Logic
Boolean Algebra: Simplifying Equations
Common Errors

## Slide 71
Common Errors
Using ticks ‘ instead of bars over variables when writing equations by hand – ticks are easy to lose
Not keeping terms aligned from step to step
  Alignment helps you see what changed from step-to-step.
  It helps in both solving and double-checking the problem.
Applying multiple theorems to the same term in one step
Applying your own personal theorems – don’t do it 
And, on a related note: almost applying the correct theorem
Not looking for opportunities to use combining, covering, and distributivity (especially the dual form).

## Slide 72
Common Errors
Losing bars (alignment will help you avoid this)
Losing terms (alignment will help you avoid this)
Trying to do multiple steps at once – this is prone to errors!
Applying theorems incorrectly, for example:
  Wrong: ABC + ABC = B Correct: ABC + ABC = AC. Products may only differ in a single term when using the combining theorem.
  Wrong: (A + A) = 0 Correct: A + A = 1
  Wrong: (A • A) = 1 Correct: A • A = 0
  Wrong: ABC = B Correct: B + ABC = B. In order to use the covering theorem, you must have a term that covers the other terms.
  Wrong: Correct: (De Morgan’s)
  Wrong: Correct: (De Morgan’s)

## Slide 73
Common Errors with De Morgan’s
Not starting from the outside parentheses and working in: this often causes additional steps.
Trying to apply De Morgan’s theorem to an entire complex operation (instead of just to terms ANDed under a bar or terms ORed under a bar)
Losing bars. Remember that applying the De Morgan’s Theorem is a 3 step process. For a product term under a bar:
  Change ANDs to ORs (or vice versa for a sum term under a bar)
  Bring down the terms
  Put bars over the individual terms
Not keeping terms associated (i.e., losing parentheses)
  For example, ABC = (A+B+C)
  Example error:
    Wrong: (ABC)’C+D’ = A’+B’+C’C + D’ = A’ + B’ + D’
    Correct: (ABC)’C + D’ = (A’+B’+C’)C + D’ = A’C+B’C + D’

## Slide 74
Chapter 2: Combinational Logic
From Logic to Gates

## Slide 75
Build the following equation using logic gates:
Y = AB + CDE
From Logic to Gates

## Slide 76
Inputs on the left (or top)
Outputs on right (or bottom)
Gates flow from left to right
Straight wires are best
Circuit Schematics Rules

## Slide 77
Wires always connect at a T junction
A dot where wires cross indicates a connection between the wires
Wires crossing without a dot make no connection
Circuit Schematic Rules (cont.)

## Slide 78
Two-level logic: ANDs followed by ORs
Example: Y = ABC + ABC + ABC
Two-Level Logic
Implements functions in SOP form

## Slide 79
Complex logic is often built from many stages of simpler gates.
Multilevel Logic

## Slide 80
Example: Priority Circuit
Output asserted
corresponding to most
significant TRUE input
Multiple-Output Circuits

## Slide 81
Priority Circuit Hardware
Y3 = A3
Y2 = A3 A2
Y1 = A3 A2 A1
Y0 = A3 A2 A1 A0

## Slide 82
Don’t Cares
Y3 = A3
Y2 = A3 A2
Y1 = A3 A2 A1
Y0 = A3 A2 A1 A0

## Slide 83
Chapter 2: Combinational Logic
Two-Level
Logic Forms

## Slide 84
ANDs followed by ORs: SOP form
ORs followed by ANDs: POS form
Only NAND gates: SOP form
Only NOR gates: POS form
Two-Level Logic Variations
Most common form of two-level logic

## Slide 85
Two-level logic variation: ORs followed by ANDs
Example: Y = (A+B)(A+B+C)
Two-Level Logic Variation
Implements functions in POS form

## Slide 86
Two-level logic: ANDs followed by ORs → NANDs
Example: Y = ABC + ABC + ABC
Two-Level Logic
Put bubbles on internal nodes.
Both: SOP form

## Slide 87
Two-level logic: ORs followed by ANDs → NORs
Example: Y = (A+B)(A+B+C)
Two-Level Logic Variation
Put bubbles on internal nodes.
Both: POS form

## Slide 88
Chapter 2: Combinational Logic
Bubble Pushing

## Slide 89
De Morgan’s Theorem
# | Theorem | Dual | Name
T12 | B•C•D… = B+C+D… | B+C+D…= B•C•D… | De Morgan’s Theorem

## Slide 90
Y = A+BC
= A•BC
= A•BC
= ABC
De Morgan’s Theorem
Work from the outside in
(i.e., top bar, then down)
Use involution when possible
Example D1:

## Slide 91
Y = A+BC+AB
= A•BC •AB
= A•BC •(A + B)
= ABC •(A + B)
= ABCA + ABCB
= ABC
DeMorgan’s Theorem
De Morgan applies to:
  Products under a bar
  Sums under a bar
Do not try to apply DeMorgan’s to a mix of operations
Example D2:

## Slide 92
Y = A+BC+AB
= A•BC •AB
= A•BC •(A + B)
= ABC •(A + B)
= ABCA + ABCB
= ABC
De Morgan’s Theorem
Example D2:
Don’t forget these parentheses!
Remember:
  AB = (A + B)

## Slide 93
Y = AB = A + B
Y = A + B = A B
De Morgan’s Theorem: Gates
NAND gate
two forms
NOR gate
two forms

## Slide 94
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output
Bubble Pushing

## Slide 95
Bubble Pushing
What is the Boolean expression for this circuit?
Y = AB + CD

## Slide 96
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel
Bubble Pushing Rules

## Slide 97
Bubble Pushing Example

## Slide 98
Chapter 2: Combinational Logic
X’s and Z’s, Oh My

## Slide 99
Contention: circuit tries to drive output to 1 and 0
  Actual value somewhere in between
  Could be 0, 1, or in forbidden zone
  Might change with voltage, temperature, time, noise
  Often causes excessive power dissipation
X is also used for:
  Uninitialized values
  Don’t Care
Warnings:
  Contention or uninitialized outputs usually indicate a bug.
  Look at the context to tell meaning
Contention: X

## Slide 100
Floating, high impedance, open, high Z
Floating output might be 0, 1, or somewhere in between
  A voltmeter won’t indicate whether a node is floating
  But if you touch the node or your instructor walks over for a checkoff, it may change randomly
Floating: Z
Tristate Buffer

## Slide 101
Floating nodes are used in tristate busses
  Many different drivers
  Exactly one is active at once
Tristate Busses

## Slide 102
Chapter 2: Combinational Logic
Karnaugh Maps

## Slide 103
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
  PA + PA = P
Karnaugh Maps (K-Maps)

## Slide 104
K-Map
Circle 1’s in adjacent squares
In Boolean expression: include only literals whose true and complement form are not in the circle
Y = AB Y = ABC+ABC = AB

## Slide 105
3-Input K-Map
Y = AB + BC
Circle 1’s in adjacent squares
In Boolean expression: include only literals whose true and complement form are not in the circle

## Slide 106
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Prime implicant: implicant corresponding to the largest circle in a K-map
Some Definitions

## Slide 107
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
K-Map Rules

## Slide 108
4-Input K-Map

## Slide 109
4-Input K-Map

## Slide 110
Chapter 2: Combinational Logic
Karnaugh Maps with Don’t Cares

## Slide 111
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
Circle a “don't care” (X) only if it helps minimize the equation
K-Map Rules

## Slide 112
K-Maps with Don’t Cares

## Slide 113
K-Maps with Don’t Cares

## Slide 114
Chapter 2: Combinational Logic
Combinational Building Blocks: Multiplexers

## Slide 115
Selects between one of N inputs to connect to output
Select input is log2N bits – control input
Example: 2:1 Mux
Multiplexer (Mux)

## Slide 116
Logic gates
  Sum-of-products form
Tristates
  Two tristates
  Turn on exactly one to select the appropriate input
2:1 Multiplexer Implementations
116

## Slide 117
4:1 Multiplexer Implementations
117
2-Level Logic
Tristates
Hierarchical
4:1 Mux Symbol

## Slide 118
Using mux as a lookup table
Logic using Multiplexers

## Slide 119
Chapter 2: Combinational Logic
Combinational Building Blocks: Decoders

## Slide 120
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Decoders

## Slide 121
Decoder Implementation

## Slide 122
OR the minterms:
Logic Using Decoders

## Slide 123
Chapter 2: Combinational Logic
Timing

## Slide 124
Delay: time between input change and output changing
How to build fast circuits?
Timing

## Slide 125
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Propagation & Contamination Delay

## Slide 126
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold
Propagation & Contamination Delay

## Slide 127
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR (max delay)
Short Path: tcd = tcd_AND (min delay)
Critical (Long) & Short Paths

## Slide 128
When a single input change causes an output to change multiple times
Glitches

## Slide 129
What happens when A = 0, C = 1, B falls?
Glitch Example

## Slide 130
Glitch Example (cont.)

## Slide 131
Fixing the Glitch

## Slide 132
Because of synchronous design conventions (see Chapter 3), glitches don’t cause problems.
It’s important to recognize a glitch: in simulations or on oscilloscope.
We can’t get rid of all glitches – simultaneous transitions on multiple inputs can also cause glitches.
Why Understand Glitches?

## Slide 133
Digital Design and Computer Architecture Lecture Notes
© 2021 Sarah Harris and David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
About these Notes